## Slide 1: UALinkAlchemy overview
Basic flows
Updated Sept 2025

## Slide 2: Motivation of this effort
The 1849 California gold rush showed suppliers of tools/equipment was lower risk to adding value and impact compared to gold-diggers.
Similarly with AI landscape, there are many efforts (quantum, in-memory-calc, etc) that will likely suffer or iterate from Amdahls law when fully implemented.
UALinkAlchemy aims to provide memory access tools for any of these efforts.

## Slide 3: MVP thoughts (or where this effort can provide value today and a few years hence)
Basic memory pooling at rack/pod scale. ~50% of platform cost in memory, how can this be shared/scaled appropriately.
Shared memory without snoop overheads (localized coherency control)
Academic HW framework of memory studies, enabling graduate-level advancements (i.e. prioritized queue latency studies)
Interfacing to novel in-memory startups (photonics/capacitive/etc)
While starting on Ethernet/UALink, can be easily adapted to CXL, NVLink, UCIe as industry evolves.
Validation block of UALink member companies.
IP interface block for “memory as a service” ASIC (i.e. Network Attached Memory NAM)
CPU/GPU/xPU IP block to attach to an SoC.

## Slide 4: Memory response variation and cache coherency scope
MC DDR
MC DDR
~40-500ns
MC UALink
~500ns
CPU or GPU
Core mesh
Smallest granularity is 64B cacheline
Low lat
High lat
As DRAM txns increase, loaded latency due to queueing with up to 500ns across all memory accesses. This is bad for real-time OS workloads and cross-VM conflicts.
Prioritized queues helps guarantee latency SLA and put lower priority access (i.e. speculative prefetch, at lower priority)
Other Skt IF
CLz
CLy
CLx

## Slide 5: MMU translation (and benefit of UALink)
Core in VM context
MMU
Physical, or Real, memory address
Core in VM context
MMU
Core in VM context
MMU
DDR MC converts to row/col addr
PCIe/CXL root port converts to IO memory space for DMA operations. TLB is managed to map to OS tables (x86=IOMMU, ARM=SMMU)
UALink

## Slide 6: C++
With OOP, stdlib.h will dynamically size arrays (i.e. new <obj>)
So if initial array size is <10> and one more object is created, then the library will autoallocate more space, i.e. <15> to grow the memory footprint.
This is to effectively perform as array grows. I.e. 12 count will be order (1) complexity. (Stdlib.h has certain preallocation algo, ignore for now.)
Upon new <obj>, stdlib malloc’s memory space of size obj. This results in a physical memory base address obj for future references. (i.e. with obj.name = “Steen”, compiler knows memory address of obj.name)
Idea is to leverage stdlib.h to do ualink.h

## Slide 7: Code mapping
C++ UALink library example
#include ualink_lib.h
New_ualink citizen record
UALinkrecord.name = “Steen”;
UALinkrecord.photo = pix.jpg;
…
Delete record
C++ app example
#include stdlib.h
new citizen record;
Record.name = “Steen”;
Record.photo = pix.jpg;
…
Delete record;
Compiler/lib translation
Record.baseaddr = malloc(64KB, RW, noswap); //results in base address for record.
Movstr record.addr <= “Steen”
//set pointer to pix.jpg
…
Free record.base
Compiler/lib translation
Scapy malloc 64KB and return record.base.addr pointer
Scapy write record.base <= “Steen”
…
Scapy free memory/deallocate
{Note that scapy is just a prototype mechanism emulating UALink protocol. Long term, there will be CPU/GPU/XPUs with direct UALink interfaces like DDRx.
I.e. Malloc returns 0x2000, and OS pagetable mapped to 0xFE500 }
This enables discussion on how existing source code can be adapted to utilize UALink-attached memory by adapting C++ stdlib.h references with ualink_lib.h references.
(I.e. DDR-only app performance compared to UALink prototype performance.)

## Slide 8
#include ualink_lib.h
AI_code_alg() Define_base dataset //now we want to convolve, m-mult, etc against 100TB of memory ualink_malloc(100TB) // now 100TB is addressable by user code For (i): AI_op (*base *^ ualink_mem(offset[i]) prefetch(ualink_mem[i+1]) end-for-i

## Slide 9: UALink FPGA overview
xPU UALink stimulus system
NIC
10GbE
Acts like a DDR DIMM
DRAM/SDRAM/Optane/SSD
xPU UALink stimulus system
NIC
10GbE
FPGA with soldered down SDRAM and DRAM
Future expansion
SCAPY tool
nf0 = close to PCIe IF

## Slide 10: Physical prototype
Stimulus system Ubuntu 18
2x 10GbE Intel x550 NIC
Virtex5 TX240T

## Slide 11: FPGA chipscope seeing an “AAAA” pkt (Sept’25) TX/RX port loopback shows .323265-.297131 = 26.1us RTT loopback hardcoded to 0, verified with port 1.
Notes: Simulus system shows in Ifconfig TX traffic on linked interface
Need to run sudo scapy
To scapy sniff : sniff(iface=“enp3s0f1", prn=lambda x: x.summary())
  Shows various DNS, ARP but they may be from other interfaces since wireshark and ifconfig is showning no RX data.
  Better to use wireshark
To scapy send: sendp(“AAAAAA", iface=“enp3s0f1", loop=1, inter=0.2)
Or in python script:
  from scapy.all import Ether, IP, UDP, sendp
  pkt = Ether() / IP(dst="192.168.0.6") / UDP(dport=12345) / b"Hello AAAA“
  pkt.show()
  sendp(pkt, iface=“enp3s0f1")

## Slide 12: Single port register response packet flow
10GMAC /XAUI
xPU UALink stimulus system Ubuntu 24.x
NIC
10GbE
SCAPY tool
nf0 = close to PCIe IF
M
S
Turbo64
Output lookup
Output Q’s
S
M
S
M
S
M
Hard-coded to nf0
Chipscope analyzer
Dean’s MAC/FMA
RISC-V as a control plane manager for data flows, security, coherency conflict
FPGA Block DRAM, dual port
I.e. “malloc” allocates addressing for 64KB R/W memory, or (on specifying MAC/FMA/etc) 32KB data/32KB result memory address space.
Other alloc addr space
FPGA 🡪
Niko’s TTS, Qbit hookups, other AI Ops…
More MAC instances
Granule64

## Slide 13: FLIT/pkt FSM flow

## Slide 14: Prototype for in-memory matrix-mult/acc
UALink mem r/w
PCIe/CXL/UCIe
 | A**B | ∑A+B | 
VecA |  |  | 
VecB |  |  | 
FPGA

## Slide 16: AXIs module options
AXI interfacing allows parallelism in dev/test/benchmark
i.e.
  in-memory-MAC with data @X[0..n] and MAC @Y[0..n]
  Convolution of X ** Y data in Z[0..n]
  Interfacing to SSD, prefetching, etc.

## Slide 17: UALink possible topology scenarios (i.e. rack level)
xPU
xPU
xPU
xPU
More distributed, localized shared mem resource (Malloc’d on demand)
Shared mem resource rack tray
More centrally shared mem resource
xPU
xPU
xPU
xPU
xPU
xPU
xPU
xPU
xPU = {CPU | GPU | IPU | DPU }

## Slide 18: Pooled memory write access
FPGA FSM
ualink_malloc(4kb)
ack
ualink_malloc(4kb)
wr64B(DEADBEEF…)
RAS/CAS signaling to memory
Memory device
Host system

## Slide 19: Pooled memory read access
FPGA FSM
ack
rd64B(addr)
RAS/CAS signaling to memory
“DEADBEEF…”
Host system
Memory device
“DEADBEEF…”

## Slide 20: Memory latency sensitivity (i.e.32GB) -> TB workloads Workload memory access frequency
L1-4cyc
L2 -8cyc
DRAM
Swap (SSD)
L3-32cyc
L1/L2/L3
UALink (500ns)
DRAM (50-500ns)

## Slide 23: Latency
Critical path | Value placeholders | Description
SCAPY generates req | 3us-est | Pre-time0, discounted
PHY NIC to FPGA | 1us-est -> 50ns | 10Gbps, scaled to 200Gbps
FPGA processing | 10cyc read write -> 1ns | Scale for FPGA mem (DRAM/SRAM…) prefetch… 100MHz to 1GHz cycles
PHY FPGA to NIC | 1us-est ->50ns | 10Gbps
SCAPY | 3us est | discounted

## Slide 24: General dev timeline
2025 : “Granule64” : SCAPY packets reading/writing 64B data. Leading to something that can be shown to VCs for ~2030 pooling product.
  Biggest dependency is SW model (library, app porting flow, a believable perf story)
  Side projects in atomicity, security, coherence resolution, queue support, SDRAM MC, DRAM MC.
2026 : “LinkPool” : RISC-V core exploration pooling cores talking to each other over AXI or ported to UALink frames.

## Slide 25: Timeline to product
Dependent on UALink CPU/GPU/xPU rollout. i.e. assume AMD server CPU with UAlink in 2029
2028: DIMM board with FPGA eval UALink pooled memory and demo workloads
2029: If funding/customers ASIC with UALink/DIMM interface

## Slide 26: Response from FPGA on read txn
FPGA generates something like below with intent that scapy captures the payload, matches the tag. Scapy or library then stores the content as the result of a ualink_read() output.
This requires FPGA to track and apply tag appropriately on responses.

## Slide 27: Kedar’s slides below
For code: Refer to the pull requests on the git repo
For this weeks update, look at
https://github.com/steenl/PortAlchemy/pull/3 (review)
https://github.com/steenl/PortAlchemy/pull/2 (merged)
The following slides shall discuss the initial frame for UAlink packets. Was able to generate packets on the wire and read using wireshark. And this framework is purely based out of simplicity - we should discuss how we want to fixate on the frame layout (easily modifiable at this point)
Currently supports Read/Write “requests” in UALink style
Week of 09/01 to 09/05, will add the “responses” parsing

## Slide 28: Frame structure for Requests
Ether layer
UALink Header
UALink Payload
Request len and request attr involve some calculations as per the UALink doc - and that’s why the user request address is converted to base address (special alignment)
Tag is needed for differentiating between requests
Op can be used to differentiate between write or read
Payload length kept to 236 to limit the total size to 256 for one request

## Slide 29: Sample request frames
0000 aa aa ab aa aa aa aa aa aa aa aa aa 08 00 10 01
0010 10 00 00 03 00 00 00 00 00 00 20 00 00 00 00 00
0000 aa aa ab aa aa aa aa aa aa aa aa aa 08 00 10 02
0010 10 00 00 1f 00 00 00 00 00 00 20 00 00 00 ff dd
0020 cc bb aa
Complete Read() request with tag 0x10, requesting 2 bytes at 0x2000
Complete Write() request frame with tag 0x10, for writing the 5 byte sized payload at 0x2000

## Slide 30: 09/27 Write request packet (w/ payload) - Link
0000 aa aa ab aa aa aa aa aa aa aa aa aa 08 00 10 02
0010 44 1c 03 ff 00 00 00 00 00 00 20 00 00 00 21 22
0020 23 24 25 26 27 28 29 00 00 00 00 00 00 00 00 00
0030 00 00 00 00 00 00 00 00 00 00 00 00
send 3 requests with different payloads - write requests
send_batch function is called twice - 3x2 = 6 packets received on wire
Dissecting the 3rd packet

## Slide 31: 09/27 Write request packet (w/ payload) - Link
0000 aa aa ab aa aa aa aa aa aa aa aa aa 08 00 10 02
0010 44 1c 03 ff 00 00 00 00 00 00 20 00 00 00 21 22
0020 23 24 25 26 27 28 29 00 00 00 00 00 00 00 00 00
0030 00 00 00 00 00 00 00 00 00 00 00 00
aa aa ab aa aa aa - destination mac
aa aa aa aa aa aa - source mac
08 00 - ether type
10 - version
02 - OP (write)
44 - transaction tag
1c - Request length
03 ff - Request attribute
00 00 00 00 00 00 20 00 - Base address
00 00 - Padding
21 22 23 24 25 26 27 28 29- Payload
Dissecting the 3rd packet
Actual packet - 256 bytes

## Slide 32: 09/28 send request and receive acks (two hosts)
Host side sending batch requests and waits for ack
FPGA simulator (receiver)
waits for write requests to be received from host -> then sends out an ack
Captured pcap on host side
shows 3 frames (for 3 write requests)
and receiving an ack in the 4th frame
Captured pcap on fpga side
shows 3 frames (for 3 write requests)
and sending back an ack in the 4th frame

## Slide 33: Memory response variation and cache coherency scope
MC DDR
MC DDR
~40-500ns
MC UALink
~500ns
CPU or GPU
Core mesh
Smallest granularity is 64B cacheline
Low lat
High lat
As DRAM txns increase, loaded latency due to queueing with up to 500ns across all memory accesses. This is bad for real-time OS workloads and cross-VM conflicts.
Prioritized queues helps guarantee latency SLA and put lower priority access (i.e. speculative prefetch, at lower priority)
Other Skt IF
CLz
CLy
CLx

## Slide 36: Steps to Linux/LibFabric or Linux/stdlibPortAlchemcy
Qemu
  Efi, osloader, Linux
  Add ACPI shim
    Define memory region non-Ram
    Adjust ACPI table
OS-boot
  Load PortAlchemy driver
App
  Configure some LibFabric workload
Run
  Snapshot + gem5 (see below)
Qemu
  Efi, osloader, Linux
  Add ACPI shim
    Define memory region non-Ram
    Adjust ACPI table
OS-boot
  Load PortAlchemy driver
  Load stdlibPortAlchemy
App
  Scapy equivalent
Run
  Snapshot + gem5 (see below)
https://www.gem5.org/assets/files/workshop-isca-2023/posters/qpoints.pdf

## Slide 37: PortAlchemy LibFabric driver
Follow OFI Provider model
Establish Address Vectors
Use default “Event” and ”Message” queues
  Either Translate Tag & Atomics to our Ualink MC I/F
  Or us NIC I/F and build off a PCI adapter theme
https://openfabrics.org/downloads/ofiwg/Industry_presentations/2015_HotI23/paper.pdf#:~:text=Libfabric%20is%20a%20library%20that%20defines%20and,supported%20on%20commonly%20available%20Linux%20based%20distributions.